## Slide 1: Permanent magnet (PM) DC motors
1
Armature
Permanent Magnets
Brushes
Commutator
Coils

## Slide 2: PMDC motors – animation

## Slide 3: PMDC motors – components
3
Notes: 3

## Slide 4: PMDC motors
Stationary element is a permanent magnet
Have commutator and brushes to switch current direction in armature
Limited in size (large magnets are expensive)
Low cost, low power, battery operation
Common in appliances, toys, RC
Electric Toothbrush

## Slide 5: Other types of DC motors
Wound Stator
  Stationary element is an electromagnet
  Connected in series or parallel with armature
  Commutator and brushes
  Can run on DC or AC current (universal motor)
Brushless
  No brushes to wear out or cause electrical noise
  More complicated to control
  Used in computer disc drives, fans
shunt wound
series wound

## Slide 6: PMDC motors
Typical Uses: Small appliances, RC, often battery powered
Often used with position or velocity feedback (optical encoder or tachometer)
Reduction gear heads common
Easy to control:
  Speed, Torque  Input voltage
Size Range:
  Micro 0.5” L x 0.2”D (pager vibrator) <$1
  Big 13”L x 4”D 2 HP $1000
RPM
Torque
V1
V2 >V1

## Slide 7: Basic principle of operation – a wire in a magnetic field will be feel a sidewise force
Conductor in a magnetic field: (Fleming’s Rule)
N
S
B = magnetic flux density
I = current
Force = I L B
F = force
Permanent
Magnet
L = length of wire
in the magnetic field

## Slide 8: In a motor, we have coils of wires, so the force becomes a moment
For each turn of the coil:
B
F
I
Torque = 2rBIL
r

## Slide 9: If you want to get more torque out of motor:
Increase L – more coils, longer armature
Stronger magnetic field (B) – use stronger magnets (typical RC airplane motors use “rare earth” magnets)
Increase current (I) – increase input voltage
Increase armature diameter, (r)

## Slide 10: Typical PMDC motor performance curves (available from the manufacturer, or by test)
Efficiency
Torque
Current
Power Out
Power In
0
wMAX
TSTALL
iSTALL
i@max
Constant V

## Slide 11: Manufacturer’s data sheet

## Slide 12: What is your design objective - maximum power or maximum efficiency?
η
Torque
W
Operates with
max power at this speed
½ No Load Speed
No Load Speed
Max Efficiency
@ this speed

## Slide 13: To size the motor, we need to know what it is driving, i.e. the “load” curve
Rotational Speed
Torque
0.5 gpm
1 gpm
2 gpm
4 gpm
8 gpm
Typical load curve
for a pump and
plumbing system,
a fan load curve is similar

## Slide 14: The intersection of the load curve and the motor curve will determine the operating speed of the motor
Rotational Speed
Torque
Load
Larger Motor
Motor A
Motor A with
2:1 reduction

## Slide 15: Other concerns
Motor Life:
  Internal losses (resulting in heat) ~ I2 This determines the maximum steady state current
  High temperature can demagnetize magnets, melt insulation
Typical gear efficiency: 70-80% for each stage

## Slide 16: Noise suppression capacitors

## Slide 17: Brushless motors
Stationary coils that are electrically
commutated
Rotating permanent magnets
In-runner – magnetic core inside coils
Out-runner – magnetic cup outside coils
Sense rotor angle using Hall effect sensors or EMF in non-powered coils
Typically three coils wired as Wye or Delta
Bidirectional coil drivers

## Slide 18: Brushless motors – stator coils, rotor PM

## Slide 19: Brushless motors - commutation

## Slide 20: Brushless motors - commutation

## Slide 21: Brushless motor – in-runner

## Slide 22: Brushless motor – out-runner
22
Magnetic
sensor
Magnet
Stationary
Coils
Circuitry to
switch coil
polarity

## Slide 23: Brushless motors – out-runner

## Slide 24: Brushless motors – out-runner

## Slide 25: Brushless motors – pancake

## Slide 26: Brushless motors – printed rotor

## Slide 27: Brushless motors – printed rotor

## Slide 28: Batteries – types
Alkaline (C, AA, AAA, 9V)
  1.5V per cell, cheap, generally not rechargeable
Lead acid (automotive)
  12V, sulphuric acid, never below 10.5V
Sealed lead acid (SLA) - gel cell, absorbed glass mat (AGM)
  6V or 12V, any orientation, never below 10.5V for 12V
NiCd (nickel-cadmium)
  1.2V per cell, may discharge completely
NiMH (nickel-metal-hydride)
  1.2V per cell, NEVER discharge completely, self-discharge
LiPo (lithium-polymer)
  dangerous charge/discharge, limited cycles ~300
LiFePO4 (lithium-iron-phosphate)
  safer, more cycles ~1000

## Slide 29: Batteries – energy density

## Slide 30: Batteries – energy density

## Slide 31: Batteries – rating
Amp-hours (Ah)
  Constant discharge current multiplied by discharge time before reaching minimum recommended voltage
C20 rating is Ah available for 20 hours
  Example: 12V gel-cell battery with 18 Ah rating can provide 0.9 A current continuously for 20 hours before reaching 10.5V minimum threshold

## Slide 32: Batteries – discharge curves
Lead acid
  More linear voltage versus time discharge curve
  Higher discharge rate reduces capacity (Peukert’s Law)
  Example: 12V gel-cell battery with 7 Ah C20 rating
    0.35 A discharge, 20 hours = 7 Ah
    0.65 A discharge, 10 hours = 6.5 Ah
    1.2 A discharge, 5 hours = 6.0 Ah
    4.2 A discharge, 1 hours = 4.2 Ah
NiCd
  Flatter voltage versus time discharge curve
  More difficult to monitor remaining capacity
  Discharge rate does not reduce capacity as much as lead acid

## Slide 33: 12V 18Ah sealed lead acid (SLA)

## Slide 34: 12V 18Ah sealed lead acid (SLA)

## Slide 35: Harbor Freight 18V NiCd battery pack

## Slide 36: Ryobi 18V NiCd Battery Pack

## Slide 37: Alkaline discharge curves

## Slide 38: NiMh and LiPo discharge curves